## Slide 1: Campus Network Security and Guest Access Control Using VLANs and Captive Portal
COMPUTER NETWORK (LAB)

## Slide 2
Submitted To:
Sir Fahad Irshad
Submitted By:
Iqra Mushtaq F2024266237
Nimra Shabir F2024266204
Mubshira Khan F2024266207
Sultan Ahmad F2024266854
Hafiz Ahmad Islam F2024266891
Mobeen Ahsan F2024266481
Spring 2026 | Computer Networks Laboratory (CN Lab) Course Project

## Slide 3
Introduction :
Modern university campuses support multiple users including students, staff, and visitors. Providing secure and controlled network access is essential to protect institutional resources.
This project implements:
Network segmentation using VLANs
Guest access isolation
Captive Portal authentication
DHCP-based IP allocation
Bandwidth control using rate limiting
Secure routing between VLANs

## Slide 4
Project Objectives
Main Goals
✔ Create separate VLANs
✔ Secure internal networks
✔ Implement Guest Isolation
✔ Develop Captive Portal
✔ Configure DHCP Services
✔ Apply Bandwidth Limitation
✔ Test Security Policies
✔ Simulate Complete Solution in GNS3

## Slide 5
Requirement | Description
VLAN 10 | Students Network
VLAN 20 | Staff Network
VLAN 99 | Guest Network
Guest Isolation | No access to Student or Staff VLAN
Captive Portal | Terms of Service Acceptance
DHCP | Automatic IP Assignment
Rate Limiting | 5 Mbps for Guests
Network Requirements:
Requirement | Description
VLAN 10 | Students Network
VLAN 20 | Staff Network
VLAN 99 | Guest Network
Guest Isolation | No access to Student or Staff VLAN
Captive Portal | Terms of Service Acceptance
DHCP | Automatic IP Assignment
Rate Limiting | 5 Mbps for Guests

## Slide 6
Network Topology Design:
Device | Quantity | Function
Cisco Router | 1 | Routing, DHCP, Rate Limiting
Cisco Switch | 1 | VLAN Management
Ubuntu Server | 1 | Captive Portal
Clients | 3 | Student, Staff, Guest
Architecture:
Router ↔ Switch ↔ VLAN Clients
Ubuntu Server connected for Captive Portal services.

## Slide 7
VLAN Implementation:
VLAN Configuration
VLAN 10 – Students
Student devices connected
Secure academic access
VLAN 20 – Staff
Administrative access
Internal services
VLAN 99 – Guests
Internet-only access
Restricted permissions
Benefits:
Better security
Reduced broadcast traffic
Easier network management

## Slide 8
Captive Portal Implementation:
Captive Portal System
Ubuntu Server Hosts
"Terms of Service" Webpage
Process:
Guest connects to Wi-Fi
Redirected to Captive Portal
Terms of Service displayed
User clicks Accept
Internet access granted
Advantages:
User agreement enforcement
Access control
Improved security

## Slide 9
DHCP and IP Address Management:
VLAN | Network Type
VLAN 10 | Students
VLAN 20 | Staff
VLAN 99 | Guests
Security and Rate Limiting: | 
Guest Isolation Guests cannot: ❌ Ping Student VLAN ❌ Access Staff Resources ❌ Reach Internal Servers Rate Limiting Guest bandwidth restricted. | 

## Slide 10
Testing and Verification:
Network Testing
Security Testing
✔ Guest unable to ping Student VLAN
✔ Guest unable to ping Staff VLAN
Captive Portal Testing
✔ Terms of Service page displayed
✔ Access granted after acceptance
Performance Testing
✔ iPerf used for bandwidth verification
✔ 5 Mbps limitation confirmed